## Slide 1: Introduction to Real Time Systems and RTOS
Lecture 19, Embedded Systems, F18

## Slide 2: Introduction to Real Time Embedded Systems
Systems that respond to external events in a timely fashion
Notes: External events can have synchronous or asynchronous characteristics. Responding to external events includes recognizing when an event occurs, performing the required processing as a result of the event, and outputting the necessary results within a given time constraint. Timing constraints include finish time, or both start time and finish time.

## Slide 3: Example
Notes: Nexperia PNX9520 processor enables vibrant media technologies in the car

## Slide 4: What is real about “real time”

## Slide 5: Real Time System

## Slide 6: Structure of Real Time System
The controlling system interacts with the controlled system in various ways.
  Periodic Interaction:
    In this case, the communication is predictable and occurs at predefined intervals.
  Aperiodic Interaction:
    the communication is unpredictable and is determined by the random occurrences of external events in the environment of the controlled system.
  combination of both types:
    The controlling system must process and respond to the events and information generated by the controlled system in a guaranteed time frame.

## Slide 7: Example: Real time weapons defense system

## Slide 8: Example: Real time weapons defense system
Command & decision system
Radar system
Weapons firing control system
Notes: The radar system scans and searches for potential targets. Coordinates of a potential target are sent to the C&D system periodically with high frequency after the target is acquired.
The C&D system must first determine the threat level by threat classification and evaluation, based on the target information provided by the radar system. If a threat is imminent, the C&D system must, at a minimum, calculate the speed and flight path or trajectory, as well as estimate the impact location. Because a missile tends to drift off its flight path with the degree of drift dependent on the precision of its guidance system, the C&D system calculates an area (a box) around the flight path.
The C&D system then activates the weapons firing control system closest to the anticipated impact location and guides the weapons system to fire continuously within the moving area or box until the target is destroyed. The weapons firing control system is comprised of large-caliber, multi-barrel, high-muzzle velocity, high-power machine guns.

## Slide 9
In this weapons defense system example, the communication between the radar system and the C&D system is aperiodic, because the occurrence of a potential target is unpredictable and the potential target can appear at any time.
The communication between the C&D system and the weapons firing control system is, however, periodic because the C&D system feeds the firing coordinates into the weapons control system periodically (with an extremely high frequency).
Initial firing coordinates are based on a pre-computed flight path but are updated in real-time according to the actual location of the incoming missile.

## Slide 10: Hard vs Soft Real time systems

## Slide 11: Hard Real Time System

## Slide 12: Soft Real Time System

## Slide 13: More Examples

## Slide 14: Real Time Operating System

## Slide 15: Introduction to RTOS
Embedded systems with moderate to large software applications require RTOS
RTOS = Real Time Operating System
A real-time operating system (RTOS) is a program that schedules execution in a timely manner, manages system resources, and provides a consistent foundation for developing application code.

## Slide 16: History
Tight integration between SW & HW
A small change in hardware might result in rewriting much of the application itself
Operating systems evolved
Abstraction of hardware from software
RTOS
VxWorks
UNIX, Windows
Notes: Unix was designed for multiuser systems
Windows was for personal computers

## Slide 17: GPOS vs RTOS
Similarities
some level of multitasking,
software and hardware resource management,
provision of underlying OS services to applications, and
abstracting the hardware from the software application.

## Slide 18: GPOS vs RTOS
Differences
better reliability in embedded application contexts
the ability to scale up or down to meet application needs
faster performance
reduced memory requirements
scheduling policies tailored for real-time embedded systems
support for diskless embedded systems by allowing executables to boot and run from ROM or RAM
better portability to different hardware platforms

## Slide 19: Components of RTOS

## Slide 20: Main components of kernel
Scheduler- is contained within each kernel and follows a set of algorithms that determines which task executes when.
Objects - are special kernel constructs that help developers create applications for real-time embedded systems. Common kernel objects include tasks, semaphores, and message queues.
Services - are operations that the kernel performs on an object or, generally operations such as timing, interrupt handling, and resource management.

## Slide 21: Scheduler
contained within each kernel
Follows algorithms to determine the time of execution of each task
Example algorithms:
  round-robin
  preemptive scheduling.
Main Topics:
schedulable entities
multitasking
context switching
dispatcher
scheduling algorithms

## Slide 22: 1. Schedulable Entities
A schedulable entity is a kernel object that can compete for execution time on a system, based on a predefined scheduling algorithm. e.g. : Tasks and Processes
TASK: an independent thread of execution that contains a sequence of independently schedulable instructions.
PROCESS: same as tasks but they provide better memory protection features, at the expense of performance and memory overhead.

## Slide 23: Schedulable Entities (contd.)
Two or more tasks or processes are simultaneously using multitasking scheme
Important Note:
  Queues and semaphores are not schedulable entities
  These items are inter-task communication objects used for synchronization and communication.

## Slide 24: 2. Multitasking
Multitasking is the ability of the operating system to handle multiple activities within set deadlines
Threads of execution appear to be running concurrently
Actually they are sequential
Context switching is fast
Notes: a thread of execution is the smallest sequence of programmed instructions that can be managed independently by a scheduler, which is typically a part of the operating system.

## Slide 25: 3. Context Switching
Context: the state of the CPU registers
Each task has its own context
A context switch occurs when the scheduler switches from one task to another.

## Slide 26: Context Switching contd.
Task – 1
Task – 1 TCB
TCB:
Task Control Block is a special data structure that stores task specific information
When task is running its context is dynamic and it is maintained in its TCB
When the task is not running, its context is frozen within the TCB, to be restored the next time the task runs.

## Slide 27
Context Switching contd.
The context of task 1 is frozen while task 2 executes, but if the scheduler needs to
run task 1 again, task 1 continues from where it left off just before the context
switch.
1. The kernel saves task 1’s context
information in its TCB.
2. It loads task 2’s context information from its TCB, which becomes the current thread of execution.
The time it takes for the scheduler to switch from one task to another is the context switch time.

## Slide 28: 4. The Dispatcher
The dispatcher is the part of the scheduler that performs context switching and changes the flow of execution.
Flow of execution/Control : Passes trough one of three areas :
  An application task
  Through an ISR
  Through the kernel

## Slide 29: The Dispatcher contd.
…
…
….
system call
…
…
..
kernel
System routines are executed
Control to kernel
Task1
Control to same or other task
…
…
..
Task2
D
D
D
The Dispatcher is doing all the context switching

## Slide 30
The Dispatcher contd.
if an ISR makes system calls,
the dispatcher is bypassed until the ISR fully completes its execution.
These context switches do not take place because the ISR must complete without being interrupted by tasks.
After the ISR completes execution, the kernel exits through the dispatcher so that it can then dispatch the correct task.

## Slide 31: 5. Scheduling Algorithms
the scheduler determines which task runs by following a scheduling algorithm (also known as scheduling policy)
  preemptive priority-based scheduling,
  round-robin scheduling

## Slide 32: Scheduling Algorithms Preemptive Priority-Based Scheduling
The task with the highest priority runs first
Real-time kernels generally support 256 priority levels, in which 0 is the highest and 255 the lowest.
Some kernels appoint the priorities in reverse order, where 255 is the highest and 0 the lowest.

## Slide 33: Preemptive Scheduling

## Slide 34: Preemptive Scheduling (contd.)
tasks are assigned a priority when they are created
a task’s priority can be changed dynamically using kernel-provided calls
This adds flexibility in embedded systems to adjust to external events as they occur, creating a true real-time, responsive system.
Misuse of this capability can lead to priority inversions, deadlock, and eventual system failure.

## Slide 35: Scheduling Algorithms Round Robin Scheduling
Round-robin scheduling provides each task an equal share of the CPU execution time
Pure round-robin scheduling cannot satisfy real-time system requirements because tasks perform work of varying degrees of importance
priority-based scheduling can be augmented with round-robin scheduling which uses time slicing to achieve equal allocation of the CPU for tasks of the same priority

## Slide 36: Round Robin Scheduling

## Slide 37: Round Robin Scheduling (contd.)
With time slicing, each task executes for a defined interval, or time slice, in an ongoing cycle, which is the round robin.
A run-time counter tracks the time slice for each task, incrementing on every clock tick. When one task’s time slice completes, the counter is cleared, and the task is placed at the end of the cycle.
Newly added tasks of the same priority are placed at the end of the cycle, with their run-time counters initialized to 0.
If a task in a round-robin cycle is preempted by a higher-priority task, its run-time count is saved and then restored when the interrupted task is again eligible for execution.

## Slide 38: Objects
Kernel objects are special constructs that are the building blocks for application development
for real-time embedded systems. Examples:
  tasks,
  semaphores
  message queues.

## Slide 39: Objects (contd.)
Tasks—are concurrent and independent threads of execution that can compete for CPU execution time.
Semaphores—are token-like objects that can be incremented or decremented by tasks for synchronization or mutual exclusion.
Message Queues—are buffer-like data structures that can be used for synchronization, mutual exclusion, and data exchange by passing messages between tasks.
concurrency, activity synchronization, and data communication.

## Slide 40: Services
operations that the kernel performs on an object
Examples:
  Timer management
  interrupt handling
  Device I/O
  resource management.

## Slide 41: Key characteristics of RTOS
reliability,
predictability,
performance,
compactness, and
scalability.

## Slide 42: characteristics of RTOS: Reliability
a reliable system is one that is available (continues to provide service) and does not fail

## Slide 43: characteristics of RTOS: Predictability
Meeting time requirements is key to ensuring proper operation
The RTOS needs to be predictable to a certain degree to satisfy real time behavior
The predictable/deterministic behavior of RTOS will give some of consistent information about the response to different system calls
In good deterministic RTOS the variance of response time to different system call should be very small.

## Slide 44: characteristics of RTOS: Performance
An embedded system must perform fast enough to fulfill its timing requirements. Typically, the more deadlines to be met—and the shorter the time between them—the faster the system’s CPU must be.
Software can also contribute to system performance.
the processor’s performance is expressed in million instructions per second (MIPS).
Throughput is the rate at which a system can generate output based on the inputs coming in. Data transfer throughput is typically measured in multiples of bits per second (bps).

## Slide 45: characteristics of RTOS: Compactness
Application design constraints and cost constraints help determine how compact an embedded system can be.
Example:
  a cell phone clearly must be small, portable, and low cost
  So limit system memory, which limits the size of the application and operating system
In such embedded systems, where hardware real estate is limited due to size and costs, the RTOS clearly must be small and efficient.

## Slide 46: characteristics of RTOS: Scalability
RTOS must be able to scale up or down to meet the application specific requirements
Depending on how much functionality is required, an RTOS should be capable of adding or deleting modular components, including file systems and protocol stacks.
Example:
Suppose that a development team wants to use an RTOS for the design of a cellular phone project and a base station project. If an RTOS scales well, the same RTOS can be used in both